## Slide 1
ID: 0x000FFFFE Data: CD 7A A6 12 9D 01 00 00
Request:
Response:
ID 0x00400021 Data: CD 7A E6 12 9D 95 00 00
Request ID
DLC (0xC8 + Number of Significant Bytes)
Address of Target ECU
Read Current Data by Identifier
Parameter Number
Requested Number of Responses
Padding
Response ID
DLC (0xC8 + Number of Significant Bytes)
Address of Responding ECU
A6 + 0x40 to Denote Response
Parameter Number
Requested Data
Padding

## Slide 2
ID: 0x0100082C Data: 0F 40 BE 07 05 90 00 00
Dashboard Brightness and Light Sensor:
Message ID
Dashboard Brightness
8 Bit Value: X X X X 1 1 1 1
Light Sensor
8 Bit Value: 0 X X X X X X X
Data I Don’t Care About
Padding (also don’t care)
I only care about this bit
I only care about the last 4 bits (lower nibble)

## Slide 3
ID: 0x19E00006 Data: 10 00 18 CA 81 9B 40 00
Ignition Status:
Message ID
Ignition Status
8 Bit Value: X 1 X X X X X X
Data I Don’t Care About
Padding (also don’t care)
I only care about this bit

## Slide 4
ID: 0x19000026 Data: 00 FF 01 40 38 11 8C 00
Cruise Control Buttons:
Message ID
Cruise Control Buttons
8 Bit Value: X X 0 X X X X X
Data I Don’t Care About
Cruise Control Cancel Button
Other Steering Wheel Buttons

## Slide 5
Network Layout:
CEM
(Central Electronics Module)
ECM (Engine Control Module)
Radio
Instrument Cluster
Door Locks
ABS Module
High Speed (500 kbps)
Low Speed (125 kbps)
To OBD2 Port
To OBD2 Port
To Other Modules
To Other Modules

## Slide 6
Wiring Diagram:
+5v and GND
LCD Display
LCD Reset Line
Asynchronous Serial
+12v and GND
Low Speed CAN (CAN0)
High Speed CAN (CAN1)
Macchina M2
To OBD Port